## Slide 1: Chapter 4: Network Layer
Chapter goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing (path selection)
  dealing with scale
  advanced topics: IPv6, mobility
instantiation, implementation in the Internet

## Slide 2: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  NAT
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 3: Network layer
on sending side encapsulates segments into datagrams
on rcving side, delivers segments to transport layer
network layer protocols in every host, router
Router examines header fields in all IP datagrams passing through it
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 4: Key Network-Layer Functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  Routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of correct left turns, right turns, exits, etc.

## Slide 5
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding

## Slide 6: Network service model
Q: What service model for “channel” transporting datagrams from sender to rcvr?
Example services for individual datagrams:
guaranteed delivery
Guaranteed delivery with less than 40 msec delay
Example services for a flow of datagrams:
In-order datagram delivery
Guaranteed minimum bandwidth to flow
Restrictions on changes in inter-packet spacing

## Slide 7: Connection setup
important function in some network architectures:
  ATM, frame relay, X.25
Before datagrams flow, two hosts and intervening routers establish virtual connection
  Routers get involved
Network and transport layer cnctn service:
  Network: between two hosts
  Transport: between two processes

## Slide 8: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 9: Network layer connection and connection-less service
Datagram network provides network-layer connectionless service
VC network provides network-layer connection service
Analogous to the transport-layer services, but:
  Service: host-to-host
  No choice: network provides one or the other
  Implementation: in the core

## Slide 10: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 11: VC implementation
A VC consists of:
  Path from source to destination
  VC numbers, one number for each link along path
  Entries in forwarding tables in routers along path
Packet belonging to VC carries a VC number.
VC number must be changed on each link.
  New VC number comes from forwarding table
Example next slide

## Slide 12: Forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
Forwarding table in
northwest router:
Routers maintain connection state information!

## Slide 13: Virtual circuits: signaling protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 14: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 15: Forwarding table
Destination Address Range Link Interface
11001000 00010111 00010000 00000000
through 0
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through 1
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through 2
11001000 00010111 00011111 11111111
otherwise 3
4 billion
possible entries

## Slide 16: Longest prefix matching
Prefix Match Link Interface
11001000 00010111 00010 0
11001000 00010111 00011000 1
11001000 00010111 00011 2
otherwise 3
DA: 11001000 00010111 00011000 10101010
Examples
DA: 11001000 00010111 00010110 10100001
Which interface?
Which interface?

## Slide 17: Datagram or VC network: why?
Internet
data exchange among computers
  “elastic” service, no strict timing req.
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
many link types
  different characteristics
  uniform service difficult
ATM
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 18: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 19: Router Architecture Overview
Two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link

## Slide 20: Input Port Functions
Decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 5

## Slide 21: Three types of switching fabrics

## Slide 22: Switching Via Memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
Input
Port
Output
Port
Memory
System Bus

## Slide 23: Switching Via a Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
1 Gbps bus, Cisco 1900: sufficient speed for access and enterprise routers (not regional or backbone)

## Slide 24: Switching Via An Interconnection Network
overcome bus bandwidth limitations
Banyan networks, other interconnection nets initially developed to connect processors in multiprocessor
Advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
  Synchronous
Cisco 12000: switches Gbps through the interconnection network

## Slide 25: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission

## Slide 26: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 27: Input Port Queuing
Fabric slower than input ports combined -> queueing may occur at input queues
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
queueing delay and loss due to input buffer overflow!

## Slide 28: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 29: The Internet Network layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 30: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 31: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 32: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 33: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 34: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 35: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 36: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
subnet

## Slide 37: Subnets
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Recipe
To determine the subnets, detach each interface from its host or router, creating islands of isolated networks. Each isolated network is called a subnet.
Subnet mask: /24

## Slide 38: Subnets
How many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 39: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 40: IP addresses: how to get one?
Q: How does host get IP address?
hard-coded by system admin in a file
  Wintel: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from server
  “plug-and-play”
(more in next chapter)

## Slide 41: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 42: Question
Alice’s IP Add: 121.36.6.13
Bob’s IP Add: 121.36.7.18
True or False?
Alice and Bob are in different subnets.

## Slide 43: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:
Note This

## Slide 44: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 45: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 46: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers

## Slide 47: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net NOT explicitly addressable, visible by outside world (a security plus).

## Slide 48: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 49: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 50: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, eg, P2P applications
  address shortage should instead be solved by IPv6

## Slide 51: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 52: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 53: Traceroute and ICMP
Source sends series of UDP segments to dest
  First has TTL =1
  Second has TTL=2, etc.
When nth datagram arrives to nth router:
  Router discards datagram
  And sends to source an ICMP message (type 11, code 0)
  Message includes name of router& IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
Destination returns ICMP “host unreachable” packet (type 3, code 3)
When source gets this ICMP, stops.

## Slide 54: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 55: IPv6
Initial motivation: 32-bit address space soon to be completely allocated.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 56: IPv6 Header (Cont)
Priority: identify priority among datagrams in flow
Flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
Next header: identify upper layer protocol for data

## Slide 57: Other Changes from IPv4
Checksum: removed entirely to reduce processing time at each hop
Options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 58: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers

## Slide 59: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4

## Slide 60: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
C
D
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
B-to-C:
IPv6 inside
IPv4

## Slide 61: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 62: Interplay between routing, forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 63: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Remark: Graph abstraction is useful in other network contexts
Example: P2P, where N is set of peers and E is set of TCP connections

## Slide 64: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path

## Slide 65: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 66: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 67: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 68: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 69: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 70: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 71: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 72: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 73: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 74: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 75: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:

## Slide 76: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
A
D
C
B
2+e
0
e
0
1+e
1
initially
… recompute
routing
… recompute
… recompute
In reality, link cost =f(traffic on link)
Does that lead to a problem?

## Slide 77: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 78: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv(y) }
where min is taken over all neighbors v of x
v

## Slide 79: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
B-F equation says:

## Slide 80: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost to each neighbor v: c(x,v)
Node x maintains Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 81: Distance vector algorithm (4)
Basic idea:
Each node periodically sends its own distance vector estimate to neighbors
When a node x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 82: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost of msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
Each node:
Does this mean a network flood
every time a link cost changes?

## Slide 83
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 84: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
At time t0, y detects the link-cost change, updates its DV,
and informs its neighbors.
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.

## Slide 85: Distance Vector: link cost changes
x
z
1
4
50
y
60
What happens now ?

## Slide 86: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
Poissoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
x
z
1
4
50
y
60

## Slide 87: Tradeoffs
What will you recommend ?
Link State?
Distance Vector?
There is no right answer

## Slide 88: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 89: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 90: Hierarchical Routing
scale: with 200 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 91: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
Gateway router
Direct link to router in another AS

## Slide 92: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Forwarding table is configured by both intra- and inter-AS routing algorithm
  Intra-AS sets entries for internal dests
  Inter-AS & Intra-As sets entries for external dests

## Slide 93: Inter-AS tasks
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
Suppose router in AS1 receives datagram for which dest is outside of AS1
  Router should forward packet towards one of the gateway routers, but which one?
AS1 needs:
to learn which dests are reachable through AS2 and which through AS3
to propagate this reachability info to all routers in AS1
Job of inter-AS routing!

## Slide 94: Set forwarding table in router 1d
Suppose AS1 learns from the inter-AS protocol that subnet x is reachable from AS3 (gateway 1c) but not from AS2.
Inter-AS protocol propagates reachability info to all internal routers.
Router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c.
Puts in forwarding table entry (x,I).
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
Subnet X

## Slide 95: Example: Choosing among multiple ASes
Learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
Use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
Hot potato routing:
Choose the gateway
that has the
smallest least cost
Determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x,I) in
forwarding table
Now suppose AS1 learns from the inter-AS protocol that subnet x is reachable from AS3 and from AS2.
To configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x.
This is also the job on inter-AS routing protocol!
Hot potato routing: send packet towards closest of two routers.
Optimal?

## Slide 96: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 97: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 98: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 99: RIP ( Routing Information Protocol)
Distance vector algorithm
Included in BSD-UNIX Distribution in 1982
Distance metric: # of hops (max = 15 hops)
D
C
B
A
u
v
w
x
y
z
destination hops
u 1
v 2
w 2
x 3
y 3
z 2
From router A to subsets:

## Slide 100: RIP advertisements
Distance vectors: exchanged among neighbors every 30 sec via Response Message (also called advertisement)
Each advertisement: list of up to 25 destination nets within AS

## Slide 101: RIP: Example
Destination Network Next Router Num. of hops to dest.
w A 2
y B 2
z B 7
x -- 1
…. …. ....
w
x
y
z
A
C
D
B
Routing table in D

## Slide 102: RIP: Example
Destination Network Next Router Num. of hops to dest.
w A 2
y B 2
z B A 7 5
x -- 1
…. …. ....
Routing table in D
w
x
y
z
A
C
D
B
Dest Next hops
w - 1
x - 1
z C 4
…. … ...
Advertisement
from A to D

## Slide 103: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 104: RIP Table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
Transprt
(UDP)
routed
physical
link
network
(IP)
Transprt
(UDP)
routed
forwarding
table

## Slide 105: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 106: OSPF (Open Shortest Path First)
“open”: publicly available
Uses Link State algorithm
  LS packet dissemination
  Topology map at each node
  Route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor router
Advertisements disseminated to entire AS (via flooding)
  Carried in OSPF messages directly over IP (rather than TCP or UDP

## Slide 107: OSPF “advanced” features (not in RIP)
Security: all OSPF messages authenticated (to prevent malicious intrusion)
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort; high for real time)
Integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains.

## Slide 108: Hierarchical OSPF

## Slide 109: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
Area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
Backbone routers: run OSPF routing limited to backbone.
Boundary routers: connect to other AS’s.

## Slide 110: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 111: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate the reachability information to all routers internal to the AS.
  Determine “good” routes to subnets based on reachability information and policy.
Allows a subnet to advertise its existence to rest of the Internet: “I am here”

## Slide 112: BGP basics
Pairs of routers (BGP peers) exchange routing info over semi-permanent TCP conctns: BGP sessions
Note that BGP sessions do not correspond to physical links.
When AS2 advertises a prefix to AS1, AS2 is promising it will forward any datagrams destined to that prefix towards the prefix.
  AS2 can aggregate prefixes in its advertisement
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 113: Distributing reachability info
With eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
1c can then use iBGP do distribute this new prefix reach info to all routers in AS1
1b can then re-advertise the new reach info to AS2 over the 1b-to-2a eBGP session
When router learns about a new prefix, it creates an entry for the prefix in its forwarding table.
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 114: Path attributes & BGP routes
When advertising a prefix, advert includes BGP attributes.
  prefix + attributes = “route”
Two important attributes:
  AS-PATH: contains the ASs through which the advert for the prefix passed: AS 67 AS 17
  NEXT-HOP: Indicates the specific internal-AS router to next-hop AS. (There may be multiple links from current AS to next-hop-AS.)
When gateway router receives route advert, uses import policy to accept/decline.

## Slide 115: BGP route selection
Router may learn about more than 1 route to some prefix. Router must select route.
Elimination rules:
  Local preference value attribute: policy decision
  Shortest AS-PATH
  Closest NEXT-HOP router: hot potato routing
  Additional criteria

## Slide 116: BGP messages
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 117: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C

## Slide 118: BGP routing policy (2)
A advertises to B the path AW
B advertises to X the path BAW
Should B advertise to C the path BAW?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!

## Slide 119: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 120: Summary: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 121
Questions?

## Slide 122: Chapter 4: Network Layer
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  Link state
  Distance Vector
  Hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 123: Broadcast Routing
R1
R2
R3
R4
source duplication
R1
R2
R3
R4
in-network
duplication
duplicate
creation/transmission
duplicate
duplicate
Deliver packets from source to all other nodes
Source duplication is inefficient:

## Slide 124: In-network duplication
Flooding: when node receives brdcst pckt, sends copy to all neighbors
  Problems: cycles & broadcast storm
Controlled flooding: node only brdcsts pkt if it hasn’t brdcst same packet before
  Node keeps track of pckt ids already brdcsted
  Or reverse path forwarding (RPF): only forward pckt if it arrived on shortest path between node and source
Spanning tree
  No redundant packets received by any node

## Slide 125: Spanning Tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) Broadcast initiated at A
(b) Broadcast initiated at D
First construct a spanning tree
Nodes forward copies only along spanning tree

## Slide 126: Spanning Tree: Creation
A
B
G
D
E
c
F
1
2
3
4
5
Stepwise construction of spanning tree
A
B
G
D
E
c
F
(b) Constructed spanning tree
Center node
Each node sends unicast join message to center node
  Message forwarded until it arrives at a node already belonging to spanning tree

## Slide 127: Multicast Routing: Problem Statement
Goal: find a tree (or trees) connecting routers having local mcast group members
  tree: not all paths between routers used
  source-based: different tree from each sender to rcvrs
  shared-tree: same tree used by all group members
Shared tree
Source-based trees
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-9

## Slide 128: Approaches for building mcast trees
Approaches:
source-based tree: one tree per source
  shortest path trees
  reverse path forwarding
group-shared tree: group uses one tree
  minimal spanning (Steiner)
  center-based trees
…we first look at basic approaches, then specific protocols adopting these approaches
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-11

## Slide 129: Shortest Path Tree
mcast forwarding tree: tree of shortest path routes from source to all receivers
  Dijkstra’s algorithm
R1
R2
R3
R4
R5
R6
R7
2
1
6
3
4
5
i
router with attached
group member
router with no attached
group member
link used for forwarding,
i indicates order link
added by algorithm
LEGEND
S: source
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-12

## Slide 130: Reverse Path Forwarding
if (mcast datagram received on incoming link on shortest path back to center)
then flood datagram onto all outgoing links
else ignore datagram
rely on router’s knowledge of unicast shortest path from it to sender
each router has simple forwarding behavior:
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-13

## Slide 131: Reverse Path Forwarding: example
result is a source-specific reverse SPT
  may be a bad choice with asymmetric links
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
datagram will be forwarded
LEGEND
S: source
datagram will not be
forwarded
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-14

## Slide 132: Reverse Path Forwarding: pruning
forwarding tree contains subtrees with no mcast group members
  no need to forward datagrams down subtree
  “prune” msgs sent upstream by router with no downstream group members
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
prune message
LEGEND
S: source
links with multicast
forwarding
P
P
P
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-15

## Slide 133: Shared-Tree: Steiner Tree
Steiner Tree: minimum cost tree connecting all routers with attached group members
problem is NP-complete
excellent heuristics exists
not used in practice:
  computational complexity
  information about entire network needed
  monolithic: rerun whenever a router needs to join/leave
Notes: Notes:
1. See L. Wei and D. Estrin, “A Comparison of multicast trees and algorithms,” TR USC-CD-93-560, Dept. Computer Science, University of California, Sept 1993 for a comparison of heuristic approaches.
3.3 Network Layer: Multicast Routing Algorithms 3-16

## Slide 134: Center-based trees
single delivery tree shared by all
one router identified as “center” of tree
to join:
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
Notes: Notes:
1. It’s always nice to see a PhD dissertation with impact. The earliest discussion of center-based trees for multicast appears to be D. Wall, “Mechanisms for Broadcast and Selective Broadcast,” PhD dissertation, Stanford U., June 1980.
3.3 Network Layer: Multicast Routing Algorithms 3-17

## Slide 135: Center-based trees: an example
Suppose R6 chosen as center:
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
path order in which join messages generated
LEGEND
2
1
3
1
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-18

## Slide 136: Internet Multicasting Routing: DVMRP
DVMRP: distance vector multicast routing protocol, RFC1075
flood and prune: reverse path forwarding, source-based tree
  RPF tree based on DVMRP’s own routing tables constructed by communicating DVMRP routers
  no assumptions about underlying unicast
  initial datagram to mcast group flooded everywhere via RPF
  routers not wanting group: send upstream prune msgs
Notes: Notes:
D. Waitzman, S. Deering, C. Partridge, “Distance Vector Multicast Routing Protocol,” RFC 1075, Nov. 1988. The version of DVMRP in use today is considerably enhanced over the RFC1075 spec.
A more up-to-date “work-in-progress” defines a version 3 of DVMRP: T. Pusateri, “Distance Vector Multicast Routing Protocol,” work-in-progress, draft-ietf-idmr-v3-05.ps
3.4 Network Layer: Internet Multicast Routing Algorithms 3-20

## Slide 137: DVMRP: continued…
soft state: DVMRP router periodically (1 min.) “forgets” branches are pruned:
  mcast data again flows down unpruned branch
  downstream router: reprune or else continue to receive data
routers can quickly regraft to tree
  following IGMP join at leaf
odds and ends
  commonly implemented in commercial routers
  Mbone routing done using DVMRP
Notes: Notes:
1. See www.mbone.com/mbone/routers.html for a (slightly outdatet) list of multicast capable routers (supporting DVMPR as well as other protocols) from various vendors.
2. ftp://parcftp.xerox.com/pub/net-research/ipmulti for circa 1996 public copy “mrouted” v3.8 of DVMRP routing software for various workstation routing platforms.
3.4 Network Layer: Internet Multicast Routing Algorithms 3-21

## Slide 138: Tunneling
Q: How to connect “islands” of multicast routers in a “sea” of unicast routers?
mcast datagram encapsulated inside “normal” (non-multicast-addressed) datagram
normal IP datagram sent thru “tunnel” via regular IP unicast to receiving mcast router
receiving mcast router unencapsulates to get mcast datagram
physical topology
logical topology
Notes: Notes:
For a general discussion of IP encapsulation, see C. Perkins, “IP Encapsulation within IP,” RFC 2003, Oct. 1996.
The book S. Bradner, A Mankin, “Ipng: Internet protocol next generation,” Addison Wesley, 1995 has a very nice discussion of tunneling
Tunneling can also be used to connect islands of IPv6 capable routers in a sea IPv4 capable routers. The long term hope is that the sea evaporates leaving only lands of IPv6!
3.4 Network Layer: Internet Multicast Routing Algorithms 3-22

## Slide 139: PIM: Protocol Independent Multicast
not dependent on any specific underlying unicast routing algorithm (works with all)
two different multicast distribution scenarios :
Dense:
group members densely packed, in “close” proximity.
bandwidth more plentiful
Sparse:
# networks with group members small wrt # interconnected networks
group members “widely dispersed”
bandwidth not plentiful
Notes: Notes:
a very readable discussion of the PIM architecture is S. Deering, D. Estrin, D. Faranacci, V. Jacobson, C. Liu, L. Wei, “The PIM Architecture for Wide Area Multicasting,” IEEE/ACM Transactions on Networking, Vol. 4, No. 2, April 1996.
D. Estrin et al, PIM-SM: Protocol Specification, RFC 2117, June 1997
S. Deering et al, PIM Version 2, Dense Mode Specification, work in progress, draft-ietf-idmr-pim-dm-05.txt
PIM is implemented in Cisco routers and has been deployed in UUnet as part of their streaming multimedia delivery effort. See S. LaPolla, “IP Multicast makes headway among ISPs,” PC Week On-Line, http://www.zdnet.com/pcweek/news/1006/06isp.html
3.4 Network Layer: Internet Multicast Routing Algorithms 3-25

## Slide 140: Consequences of Sparse-Dense Dichotomy:
Dense
group membership by routers assumed until routers explicitly prune
data-driven construction on mcast tree (e.g., RPF)
bandwidth and non-group-router processing profligate
Sparse:
no membership until routers explicitly join
receiver- driven construction of mcast tree (e.g., center-based)
bandwidth and non-group-router processing conservative
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-26

## Slide 141: PIM- Dense Mode
flood-and-prune RPF, similar to DVMRP but
underlying unicast protocol provides RPF info for incoming datagram
less complicated (less efficient) downstream flood than DVMRP reduces reliance on underlying routing algorithm
has protocol mechanism for router to detect it is a leaf-node router
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-27

## Slide 142: PIM - Sparse Mode
center-based approach
router sends join msg to rendezvous point (RP)
  intermediate routers update state and forward join
after joining via RP, router can switch to source-specific tree
  increased performance: less concentration, shorter paths
R1
R2
R3
R4
R5
R6
R7
join
join
join
all data multicast
from rendezvous
point
rendezvous
point
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-28

## Slide 143: PIM - Sparse Mode
sender(s):
unicast data to RP, which distributes down RP-rooted tree
RP can extend mcast tree upstream to source
RP can send stop msg if no attached receivers
  “no one is listening!”
R1
R2
R3
R4
R5
R6
R7
join
join
join
all data multicast
from rendezvous
point
rendezvous
point
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-29

## Slide 144: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?